## Slide 1: Studying the Effect of Network Latency on an Adaptive Coordinated Path Planning Algorithm for UAV Platoons
Baisakhi Chatterjee & Rudra Dutta

## Slide 2: INTRODUCTION
Autonomous Unmanned Aerial Vehicles can perform a variety of tasks
    Network Coverage
    Search and Rescue
    Traffic Surveillance
Thus, communication in autonomous UAVs for dynamic path planning is an area of considerable research interest

## Slide 3: OBJECTIVES
Study mission-oriented behaviour in UAV platoons
    Mission-orientation implies trajectories are adaptively planned by UAVs, cannot be pre-planned
    In turn requires messages to allow UAVs in platoon to coordinate
FOCUS – Study the dependence on Communication
    Messages utilized for information exchange
    Evaluate relationship between message dependence and task parameters
    Consider real world challenges like message delay

## Slide 4: METHODOLOGY
The algorithmic approach depends on the task chosen
Choice of task – Plume Wrapping
    Problem of finding the boundary of a gaseous, possibly toxic, plume
    Multi-UAV communication using messages
    Adaptive trajectory planning based on dynamic data
We develop an algorithm to –
    Study message dependance on path planning
    Investigate the result of bounded variable delay in communication

## Slide 5: WHY PLUME WRAPPING?
Plume wrapping is a practical problem in real world scenario
Problem solution requires a fully autonomous UAV group
Communication between UAVs is essential to coordinate decisions
Adaptive path planning based on dynamically sensed data

## Slide 6: ASSUMPTIONS
The plume is spherical in shape
The concentration is monotonically decreasing from the center to the boundary
High level abstraction of communication medium has been considered
UAV platoon starts from an arbitrary location inside the plume
Each UAV has a unique ID, represented by a numerical value
The ID Numbers are sequential, starting from 0

## Slide 7
ALGORITHM

## Slide 8: OUTLINE
A single UAV detects the boundary
Every other UAV moves to form a sphere
The sphere Expands and Rotates till the plume is surrounded
Stops when every UAV reaches the boundary

## Slide 9: DESIGN
Initialization
Initial Sphere Formation
Stop-Click Phase
Termination

## Slide 10: INITIALIZATION
UAVs are placed in an arbitrary configuration
A single UAV starts to move
UAV samples the plume density periodically
Stops at boundary – Anchor Point
Broadcasts message to other UAVs
I should start moving
Boundary Not Reached
Boundary Still Not Reached
Boundary
Reached!

## Slide 11: INITIAL SPHERE FORMATION
Anchor UAV broadcasts message
Other UAVs calculate target position on a sphere at origin
UAVs translate sphere to the boundary
UAVs move to the target position
Boundary
Reached!
Awesome
Great!

## Slide 12: PLACING N POINTS ON A SPHERE
We have used Fibonacci Spiral Method
Fibonacci Spiral method projects 2D Fibonacci lattice to 3D spheres
Benefits –
    Fast, easy to implement
    Relies on unique ID, allows for distributed implementation

## Slide 13: EXPANSION & ROTATION
Expansion
    Movement of every UAV such that radius of the Fibonacci Sphere is increased
    Occurs when every point is INSIDE the plume boundary
Rotation
    Movement of every UAV such that Fibonacci Sphere moves towards the plume
    Occurs when at least one point is OUTSIDE the plume boundary
Anchor Point does not move

## Slide 14: EXPANSION & ROTATION – INITIAL APPROACH
Expansion and Rotation are mutually exclusive operations
The operation is triggered when an UAV receives positional updates from every other member
Ideally, each UAV makes the same series of choices
In reality, the platoon loses synchronization, and the algorithm often fails to converge
This led to our second choice – forced synchronization, or Stop-Click Phase

## Slide 15: STOP-CLICK PHASE
Each round has 2 turns – Stop and Click
STOP
    This phase is triggered when the UAV has received updates from all group members
    Once all updates are received, UAV calculates next target position
    The UAV then broadcasts its current position and density
CLICK
    During this phase, the UAV again waits to receive updates from group members
    Each UAV begins moving to their target destination
    Once the UAV has reached the position it stops moving
    The UAV then broadcasts its current position and density

## Slide 16: STOP-CLICK PHASE
Last UAV broadcasts position
Initial Fibonacci Sphere Formed
STOP Phase
16
Every UAV receives message
Every UAV calculates next target position
Position Updates from all members received
Every UAV broadcasts position
CLICK Phase
Every UAV receives message
Every UAV moves to target position
Position Updates from all members received
Every UAV broadcasts position
Reached!
STOP Phase
Every UAV receives message
Every UAV calculates next target position
Position Updates from all members received
Every UAV broadcasts position
Every UAV is inside the plume
Expansion Chosen
One UAV is outside the plume
Rotation Chosen
CLICK Phase
Every UAV receives message
Every UAV moves to target position
Position Updates from all members received
….And so on

## Slide 17: INITIAL APPROACH vs STOP-CLICK PHASE
INITIAL APPROACH
Fast approach
No synchronization, hence message delay does not build up
Will not stall in case of message or UAV loss
Does not provide a good distribution
Does not always converge
STOP-CLICK PHASE
Slower approach
Message delay builds up faster
Will stall in case of message or UAV loss
Provides a good distribution
Always converges
Algorithm Converged Bad Distribution
Algorithm Converged Good Distribution
Algorithm did not Converge
Algorithm Converged Good Distribution

## Slide 18: TERMINATION
Every UAV is INSIDE the plume  Expansion
At least one UAV is OUTSIDE the plume  Rotation
Every UAV is at the Boundary Region  No Movement
No change in two successive Stop-Click rounds  Algorithm Terminates

## Slide 19: WORKING EXAMPLE

## Slide 20
RESULTS

## Slide 21: SIMULATION ENVIRONMENT
We designed a Discrete Event Simulation in JAVA
An independent Engine is responsible for executing events from a list
Events are of three types –
    Broadcast Message Event
    Transmit Message Event
    Receive Message Event
A single Broadcast Message Event is provided as seed
Seed Event
Event 1, T=0
Event 2, T=2
Event 3, T= 10
Event 4, T= 15
No New Event
Event 5, T= 12
End Simulation
No New Event

## Slide 22: SIMULATION CRITERIA
We tested our algorithm on the following criteria –
  Time taken to form the initial Fibonacci sphere
  Total time taken
  Total Number of Messages exchanged
  Standard Deviation of the solid angle subtended by each UAV
      We plotted a 3D Voronoi Cell Mapping for each UAV
      We calculated the solid angle for each cell

## Slide 23: TESTING SCENARIO
To judge the robustness, we tested our code on the following scenarios –
    Number of UAVs
      No Message Delay
      Constant Message Delay
      Variable Message Delay (Bounded)
    Plume Radius
    Boundary Region
    Initial Fibonacci Sphere Radius
Each scenario was executed 50 times
Baseline
Variable
Message
Delay

## Slide 24: MESSAGE DELAY
Messages may be delayed due to a variety of factors –
    Message takes longer route through multi-hop path
    Message is lost and needs to be retransmitted
    Message transmission is delayed at sender or intermediate node by queueing
We have proposed a high level abstraction of delay
Message delay is an approximation of non-deterministic delay

## Slide 25: MESSAGE DELAY DISTRIBUTION

## Slide 26: Time Taken
Variable No of UAVs –
No Message Delay
Variable No of UAVs –
Constant Message Delay
Variable No of UAVs –
Variable Message Delay
Variable Plume Radius –
Variable Message Delay
Variable Plume Boundary –
Variable Message Delay
Variable Initial Radius –
Variable Message Delay

## Slide 27: Total No of Messages
Variable No of UAVs –
No Message Delay
Variable No of UAVs –
Constant Message Delay
Variable No of UAVs –
Variable Message Delay
Variable Plume Radius –
Variable Message Delay
Variable Plume Boundary –
Variable Message Delay
Variable Initial Radius –
Variable Message Delay

## Slide 28: Standard Deviation of UAV Cell Angle
Variable No of UAVs –
No Message Delay
Variable No of UAVs –
Constant Message Delay
Variable No of UAVs –
Variable Message Delay
Variable Plume Radius –
Variable Message Delay
Variable Plume Boundary –
Variable Message Delay
Variable Initial Radius –
Variable Message Delay

## Slide 29: NUMBER OF UAV – NO MESSAGE DELAY

## Slide 30: NUMBER OF UAV – CONSTANT MESSAGE DELAY

## Slide 31: VARIABLE UAV GROUP SIZE

## Slide 32: VARIABLE PLUME RADIUS

## Slide 33: VARIABLE BOUNDARY REGION

## Slide 34: VARIABLE INITIAL FIBONACCI SPHERE RADIUS

## Slide 35: VARIABLE UAV GROUP SIZE

## Slide 36: VARIABLE PLUME RADIUS

## Slide 37: VARIABLE BOUNDARY REGION

## Slide 38: VARIABLE INITIAL FIBONACCI SPHERE RADIUS

## Slide 39: DISCUSSION - CONFIDENCE INTERVAL
We expected confidence intervals with a larger margin of error
In practice, margin of error was very small
Reason - Synchronization in the Stop-Click Phase
UAVs wait for the last member of the group to finish broadcasting

## Slide 40: DISCUSSION - CONFIDENCE INTERVAL

## Slide 41: DISCUSSION - CONFIDENCE INTERVAL
What if we remove the synchronization?
Unfortunately the algorithm does not converge in most cases
But in the cases it does ….

## Slide 42
CLOSING REMARKS

## Slide 43: SUMMARY
We have presented a detailed study on communication and coordination in a group of autonomous UAVs
We have evaluated the dependance of the algorithm on information exchange
And we have shown that a task can be successfully complicated despite presence of variable (bounded) message delays
Our findings, however, show that there is a trade-off between ensuring correctness and overall mission delay

## Slide 44: FUTURE WORK
Consider Message Loss
Limit Communication Range
Implement Multi-Hop message passing
Introduce Parallel Movement of UAVs during Initial Sphere Formation Phase
Study other problems in general area of communication for aerial platoon coordination

## Slide 45: Thank you