## Slide 1: Guaranteeing Partial State Synchronization for UAV Platoon under Message or UAV Loss
Baisakhi Chatterjee & Dr. Rudra Dutta
Department of Computer Science, North Carolina State University, USA

## Slide 2: INTRODUCTION
Autonomous Multi-UAV Groups have a variety of applications
    Network Coverage
    Search and Rescue
    Traffic Surveillance
Thus, communication in autonomous UAVs for dynamic path planning is an area of considerable research interest
Notes: Autonomous Multi-UAV Groups have a variety of applications
Network coverage is the problem of optimizing the placement of mobile stations to increase connectivity between groups of users. UAVs are uniquely suited for this task.
Another activity where UAVs thrive is that of Search and Rescue. UAVs can locate groups of survivors in potentially dangerous conditions and alert rescue organizations.
Traffic surveillance, too benefits from the UAVs usage. These devices can monitor traffic patterns and detect anomalous behaviours.

## Slide 3: MOTIVATION
In our previous work, we focused on studying the dependence of communication on mission correctness
Exemplar of Plume Wrapping
    Problem of finding the boundary of a gaseous, possibly toxic, plume
    Multi-UAV communication & adaptive trajectory planning based on dynamic data
Previously, we considered an abstract high-level view of the communication channel
In this work, we have modeled a real-world lossy channel.
The goal of our research is to show that we can guarantee partial multiparty synchronization in a distributed autonomous system
Notes: While it is reasonable to assume that the starting phase of a plume with pollutants lighter than air will assume a roughly spherical shape [11], this technique poses a challenge when the contaminants are heavier than air and drop to the ground.

## Slide 4
ALGORITHM

## Slide 5: DESIGN
Initialization
Initial Sphere Formation
Stop-Click Phase
Termination

## Slide 6: OVERVIEW
Initialization
    UAVs are placed in an arbitrary configuration
    A single UAV searches for the boundary
    Stops and broadcasts message to other UAVs when boundary is detected
Initial Sphere Formation
    Other UAVs calculate target position on a sphere at origin using Fibonacci Sphere Formula
    UAVs translate sphere to the boundary
    UAVs move to the target position

## Slide 7: OVERVIEW
Stop-Click Phase
    Synchronization Phase where each UAV waits for n updates to make a ‘decision’.
    STOP is triggered when the UAV has received updates from all group members
    During CLICK, the UAV moves to its target point
    For plume wrapping, decisions are Expansion or Rotation
Termination
    The algorithm finishes when every other UAV is a the boundary region

## Slide 8: EXPANSION & ROTATION
Expansion
    Movement of every UAV such that radius of the Fibonacci Sphere is increased
    Occurs when every point is INSIDE the plume boundary
Rotation
    Movement of every UAV such that Fibonacci Sphere moves towards the plume
    Occurs when at least one point is OUTSIDE the plume boundary

## Slide 9: SYNCHRONIZATION LOSS
As is evident, Stop-Click Phase requires multiparty synchronization
This is made difficult due to
    Message Loss as a result of unreliable channel
    UAV Loss due to system fault
The problem can be generalized to any UAV platoon mission where agents require updated state knowledge.
Our algorithm guarantees partial multi-party synchronization

## Slide 10: SYNCHRONIZATION LOSS
10
Reached!
Every UAV is inside the plume
Expansion Chosen
One UAV is outside the plume
Rotation Chosen
Message is not delivered
Incorrect Decision Taken
Ideal Conditions
Message Loss

## Slide 11: MULTI-PARTY SYNCHRONIZATION
Three key components are added to ensure partial multi-party synchronization.
Sequence Numbers – Enforces order on states and limits desynchronization.
Message Retransmission Timer – Retransmits Message after a certain time.
UAV Loss Timer – Marks UAV as lost after it has not been heard from for a long time.
N
Y
Recv
Msg from UAVX?
UAVX Timer Expired?
N Msgs Recvd for State?
Next State
Mark UAVX Lost

## Slide 12: SEQUENCE NUMEBRS
Maintains current state information
States are monotonically increasing
Messages are accepted based on state information
If current state of UAVX is P, it has received all (P-1)th messages from neighbors and will only accept Pth messages
If some UAVY has received all Pth messages, it will advance to (P+1)
Guarantees Bounded Variation in States
Notes: No Message Loss
  Each UAV starts with n tokens which are consumed during state change
  n tokens are then received via state information
Message Loss
  Message from UAVk to UAVj is lost
  UAVj is thus stalled thinking UAVk is still at Sp-1

## Slide 13: Message Retransmission
Retransmit messages for a state after timer expires
Message contains information about current and previous state
If UAVX is at state P, other UAVs are at (P-1), P or (P+1)
UAVs at (P+1) ignore this message
UAVs at P accept this message
UAVs at (P-1) extract previous state info

## Slide 14: UAV Loss
N-bit timer for each UAV, including self
Keeps track of how often one agent has heard from other agents
If some UAV has not communicated for a long time, the UAV is marked as lost, and subsequent messages from the UAV are rejected.
Tamp Down Mode – When a UAV is marked as “Lost” all other UAVs Tamp Down for a time and reject all messages
    This allows every UAV time to mark the offending UAV as lost
Agile Mode – UAVs purge the existing state information and rebuilt the Information Data structure, accepting messages only from UAVs who have also marked the offending UAV as “Lost”

## Slide 15: WORKING EXAMPLE
Message is not delivered
Retransmission Occurs
Message Loss
UAV suffers Transmitter Fault
Other UAVs wait till Timeout
UAV Loss
Correct Decision is Taken
Faulty UAV Aborts Mission
Other UAVs take a decision without faulty UAV’s data

## Slide 16
RESULTS

## Slide 17: Time Taken

## Slide 18: Time Per Round

## Slide 19: Time - UAV Loss

## Slide 20
CLOSING REMARKS

## Slide 21: SUMMARY & FUTURE WORK
We have designed an algorithm that guarantees partial synchronization in a distributed multiparty system
Our algorithm is generic and can be applied to platoons engaged in any mission that requires state coordination via sharing of information
Through an exemplar problem, we have shown that our algorithm guarantees mission completion and correctness.
In future, we plan to adapt our approach to the case of limited UAV-to-UAV communication range and multi-hop communications.
It would also be of interest to demonstrate an approach for allowing UAV failures to be temporary,

## Slide 22: Thank you